## Slide 1
Vyond: Flexible and Rapid WorldGuard-Based
Security Prototyping using Chipyard
Sungkeun Kim
Samsung Research
Hardware Isolation Primitives
for Trusted Execution Environments (TEEs)
1. Prevent Unauthorized Access
Ensures that sensitive code and data are isolated from untrusted SW, including OS and hypervisor
2. Minimize Trusted Computing Base (TCB)
HW primitives enable smaller and more verifiable TCBs by enforcing boundaries at the HW level
3. Enforce Strong Access Control
HW isolation provides robust access control mechanisms that SW alone cannot guarantee
1. Generators for WorldGuard Marker and Checker
- Easy to configure and place markers and checkers
2. Support for different security design phase - Simulation, FPGA, and QEMU
- Security designer can use a proper setup depending on their design phase
3. Example configurations and test programs
- They can be references of a security monitor
- One example found a potential issue on WorldGuard specification (reported to Security TG)
4. Reference Security Monitor
- A security monitor that protects enclaves using WorldGuard (WG)
Key Features of Vyond
Collaboration of PMP and WorldGuard for complete isolation
- To Protect statically allocated regions (SM, I/O devices)  WorldGuard
No extra works is required for enclave migration (e.g., PMP register update)
Useful in Robot, Car, and IoT devices with many sensors
- To protect dynamically allocated regions (OS, Enclaves)  PMP
As PMP is per-core solution, it is easy for SM to reallocate memory region for different enclave.
Configurable Hardware Isolation for Fast Prototyping
Enables Rapid Prototyping
Configurable WorldGuard Implemented
1. Implemented WorldGuard Specification (v4.0)
- Implemented WorldGuard Checkers (WGC) and Markers (WGM)
- Extended Rocket Core (CSRs, TLB, and Caches), Inclusive Cache (LLC)
2. WorldGuard as Chipyard generator
- Minimum changes in Chipyard to be part of Chipyard
Security Prototyping with WorldGuard on Chipyard
https://www.github.com/Samsung/vyond
sk84.kim@samsung.com
Contact :
References :
1. https://lists.riscv.org/g/security/attachment/711/0/worldguard_rvia_spec-v0.4.pdf
2. https://github.com/ucb-bar/chipyard
3. https://patchwork.ozlabs.org/project/qemu-devel/cover/20240612081416.29704-1-jim.shu@sifive.com
Vyond
Use Cases and Future Potential
WorldGuard Checker Configuration for PLIC
WorldGuard Checker Placement between PLIC and Bus
App1
HW
Resource
Isolation IP
App2
U-mode
S-mode
M-mode
HW
SW
App1
App2
DRAM
Untrusted
OS
Malicious Code
Security Monitor
Vyond
Not configurable
No WorldGuard Implemented
BUS
Security Monitor (SM)
IO Device
OS
World 3
Enclave 1
Enclave 2
DRAM
PMP
Hart
World 1
wgMarker
wgChecker
wgMarker
OS
App
App
App
World 3
World 1
IO Device
wgChecker
World 2
Enclave 1
World 1
PMP-isolated regions
WG-isolated regions
Enclave 2
World 2
World 2