## Slide 1: WorldGuard: Software Isolation in RISC-V and Vyond
Sungkeun Kim
Security&Privacy Team
Samsung Research
July31, 2025

## Slide 2: About me
Working on security in computer systems and architecture
  Thesis – Cache Design and Analysis for Mitigating Hardware Security in Multicore Systems
Developed on Galaxy phones before Ph.D. study
  Android framework
Like open-source projects
  H2database, Gem5, Intel RAAD, Chipyard
  Now vyond
Like Running

## Slide 3: Vyond: Flexible and Rapid WorldGuard-based Security Prototyping using Chipyard

## Slide 4: Agenda
Software (Runtime) isolation for Trusted Execution Environment
WorldGuard Introduction
WorldGuard Implementation on Chipyard
Related techniques and future potential

## Slide 5: Trusted Execution Environment

## Slide 6: What’s wrong with my phone?
What’s wrong with my phone and server?
  We can do so many things with it.
    Banking, games, videos, etc.
  Might be something malicious together..
    A larger attack surface
It may happen the same thing in clouds services
  Many services from different companies run in the physically the same machine
Sharing the physical resource is efficient but dangerous!
Notes: What is wrong with my phone?
At one level, nothing. It is a superb device that can do hundreds of tasks that once upon a time you needed multiple devices to achieve… but therein lies a problem.
With that ability to do many tasks comes masses of software. The more software, the larger the number of places where there may be a security issue (a larger “attack surface”) and the higher the likelihood that vulnerabilities will be found. To work around that issue, the Trusted Execution Environment (TEE) was developed by a consortium of concerned parties; from network operators, through manufacturers, to OS vendors.

## Slide 7: Trusted Execution Environment
Guarantees Integrity and Confidentiality
Examples
  Intel – SGX/TDX
  Arm – TrustZone/Realms
  RISC-V – Keystone/Pengai
  Samsung – TrustWare (Tursted OS)
WorldGuard provides isolation
https://www.trustonic.com/technical-articles/what-is-a-trusted-execution-environment-tee/
Notes: A Trusted Execution Environment (TEE) is an environment for executing code, in which those executing the code can have high levels of trust in the asset management of that surrounding environment because it can ignore threats from the “unknown” rest of the devicei. Hence TEE stands for Trusted Execution Environment and to distinguish them from the uncertain nature of applications in the REE (REE? Wait a second…), applications in the TEE are known as Trusted Applications (TAs). Generally, the rest of the device hosts a feature Rich OS like Android™, and so is generically known in this context as the REE (Rich Operating System Execution Environment).
Trust in a Trusted Execution Environment (TEE)
There are many interpretations of what is meant by Trust. In the TEE it is used to imply that you may have a higher level of trust in validity, isolation and access control in items (assets) stored in this space, when compared to more general purpose software environments. This then ripples down to an assertion that the Trusted OS and Trusted Applications executing inside that space are more trustworthy.
Why is a Trusted Execution Environment more Trustworthy?
Secure start-up
In the TEE, that Trust requires that all TEE related assets, code, the underlying Trusted OS and its support code, have been installed and started through a methodology that requires its initial state to be as expected by the designers (i.e. EVERYTHING is signature checked, immutable, or held in isolation).
TEEs only accept code for execution that has been:
Appropriately authorized
And where that authorization has been checked by other authorized code
And that includes everything from after ROMii boot
(you can consider the ROM code authorized by its presence).
TA’s can only directly access their own data (including key) assets:
There is no method for a TA to directly access assets of other TAs or other components of the TEE.

## Slide 8: Taxonomy of Isolation strategies
Partitioning Resources
https://arxiv.org/pdf/2205.12742
Notes: A Trusted Execution Environment (TEE) is an environment for executing code, in which those executing the code can have high levels of trust in the asset management of that surrounding environment because it can ignore threats from the “unknown” rest of the devicei. Hence TEE stands for Trusted Execution Environment and to distinguish them from the uncertain nature of applications in the REE (REE? Wait a second…), applications in the TEE are known as Trusted Applications (TAs). Generally, the rest of the device hosts a feature Rich OS like Android™, and so is generically known in this context as the REE (Rich Operating System Execution Environment).
Trust in a Trusted Execution Environment (TEE)
There are many interpretations of what is meant by Trust. In the TEE it is used to imply that you may have a higher level of trust in validity, isolation and access control in items (assets) stored in this space, when compared to more general purpose software environments. This then ripples down to an assertion that the Trusted OS and Trusted Applications executing inside that space are more trustworthy.
Why is a Trusted Execution Environment more Trustworthy?
Secure start-up
In the TEE, that Trust requires that all TEE related assets, code, the underlying Trusted OS and its support code, have been installed and started through a methodology that requires its initial state to be as expected by the designers (i.e. EVERYTHING is signature checked, immutable, or held in isolation).
TEEs only accept code for execution that has been:
Appropriately authorized
And where that authorization has been checked by other authorized code
And that includes everything from after ROMii boot
(you can consider the ROM code authorized by its presence).
TA’s can only directly access their own data (including key) assets:
There is no method for a TA to directly access assets of other TAs or other components of the TEE.

## Slide 9: Taxonomy of Isolation strategies
Enforcement
  Logical
  Cryptographical
https://arxiv.org/pdf/2205.12742
Notes: A Trusted Execution Environment (TEE) is an environment for executing code, in which those executing the code can have high levels of trust in the asset management of that surrounding environment because it can ignore threats from the “unknown” rest of the devicei. Hence TEE stands for Trusted Execution Environment and to distinguish them from the uncertain nature of applications in the REE (REE? Wait a second…), applications in the TEE are known as Trusted Applications (TAs). Generally, the rest of the device hosts a feature Rich OS like Android™, and so is generically known in this context as the REE (Rich Operating System Execution Environment).
Trust in a Trusted Execution Environment (TEE)
There are many interpretations of what is meant by Trust. In the TEE it is used to imply that you may have a higher level of trust in validity, isolation and access control in items (assets) stored in this space, when compared to more general purpose software environments. This then ripples down to an assertion that the Trusted OS and Trusted Applications executing inside that space are more trustworthy.
Why is a Trusted Execution Environment more Trustworthy?
Secure start-up
In the TEE, that Trust requires that all TEE related assets, code, the underlying Trusted OS and its support code, have been installed and started through a methodology that requires its initial state to be as expected by the designers (i.e. EVERYTHING is signature checked, immutable, or held in isolation).
TEEs only accept code for execution that has been:
Appropriately authorized
And where that authorization has been checked by other authorized code
And that includes everything from after ROMii boot
(you can consider the ROM code authorized by its presence).
TA’s can only directly access their own data (including key) assets:
There is no method for a TA to directly access assets of other TAs or other components of the TEE.

## Slide 10: WorldGuard

## Slide 11: Introduction to WorldGuard (WG)
A hardware-based software isolation solution for RISC-V cores
It leverages logical enforcement strategy to isolate
WG provides software execution contexts known as "worlds", beyond which software cannot reach.
  World is referred to World ID (WID)

## Slide 12: Key Concepts
A wg-aware core
  Contains WID registers needed to mark transactions with WID associated with each active privilege level.
A wgMarker
  Adds the active WID to bus transaction passing through them.
A wg checker
  Accept or reject transactions based on:
    Physical address, WID, transaction type (read or write)
    Accepted transaction are passed downstream to the target resource.
    Rejected transaction generates an interrupt or exception.
The trusted World ID
  WID authorized to access WG configuration registers.

## Slide 13: Overview

## Slide 14: A wg-aware core (CSR+Marker)
A WG-aware core integrates wgMarker with additional internal registers and CSRs so that different privilege modes use different WIDs.
WID CSRs

## Slide 15: Worlds allocation example
Security Monitor (SM)
World 7
Operating System
World 6
App
World 1
App
App
App
World 3
App
App
App
World 2
App
App
S/W
M-mode
S-mode
U-mode
Not running
Running

## Slide 16: Worlds allocation example
Security Monitor (SM)
World 7
Operating System
World 6
App
World 1
App
App
App
World 3
App
App
App
World 2
App
App
S/W
H/W
M-mode
S-mode
U-mode
WG CSR
Control
Logic
wid
WG-Aware Core
Not running
Running
mlwid
?
mwiddeleg
?
slwid
?
WG CSRs

## Slide 17: Worlds allocation example
Security Monitor (SM)
World 7
Operating System
World 6
App
World 1
App
App
App
World 3
App
App
App
World 2
App
App
S/W
H/W
M-mode
S-mode
U-mode
WG CSR
Control
Logic
wid
WG-Aware Core
Not running
Running
mlwid
0b00001110
mwiddeleg
0x6
slwid
?
① Booting

## Slide 18: Worlds allocation example
Security Monitor (SM)
World 7
Operating System
World 6
App
World 1
App
App
App
World 3
App
App
App
World 2
App
App
S/W
H/W
M-mode
S-mode
U-mode
WG CSR
Control
Logic
wid
WG-Aware Core
Not running
Running
mlwid
0b00001110
mwiddeleg
0x6
slwid
0x2
② Context Switch

## Slide 19: WID selection logic

## Slide 20: wgChecker
The checker monitors a fixed physical address range reject or accept the transaction.
  Reject: interrupt / exception
  Accept: send the transaction to downstream
Slots can specify a rule for a contiguous subset of addresses
  Read/Write permissions for each world

## Slide 21: wgChecker – Configuration Register

## Slide 22: wgChecker – Slot Register

## Slide 23: wgChecker – Rule register

## Slide 24: BootROM and wgChecker
0x6004000
ROM
wgc_rom
0x0001_0000
Configuration:
m-mode (WID 7) can read the entire ROM region.
For RW without the permission, raise bus interrupt.
NAPOT for addressing encoding
0x5fff
0b10 00 00 00 00 00 00 00
0xc02
address
perms
cfg
0x0
0x8
0x10
0
2
0
1
0
0
1
1
0
2
8
9
10
11
7
31
A
ER
EW
IR
IW
L
Slot[1]
0x0001_ffff

## Slide 25: DRAM and wgChecker

## Slide 26: DRAM and PMP

## Slide 27: WorldGuard Implementation on Chipyard

## Slide 28: What is chipyard?
A unified framework for agile generator-based SoC development
It provides a kind of glue for a general SoC design to connect target design flows
Key features:
  Chisel - Reusable by a high-level HDL.
  Single source multiple targets
    FPGA, Simulation, ASIC
  Ecosystem – many available generators
    AI Accelerators – Gemmini, NVDLA
    RISC-V Cores – Rocket, Boom, Ibex

## Slide 29: Quick Prototyping: generators on top of standard library
https://www2.eecs.berkeley.edu/Pubs/TechRpts/2022/EECS-2022-247.pdf

## Slide 30: Chisel – Hardware Construction Language
Chisel is a hardware construction language embedded in Scala that lets you write flexible, type-safe, and reusable code to generate Verilog for digital circuit design.
Clock and Reset is automatically wired-up
Bulk IO connection is possible (e.g., IO Bundle)
Parameterized Modules

## Slide 31: Chisel – Hardware Construction Language (example)
CPU Top

## Slide 32: Chisel – Hardware Construction Language (example)
Timer

## Slide 33: Single source multiple targets
https://www2.eecs.berkeley.edu/Pubs/TechRpts/2022/EECS-2022-247.pdf

## Slide 34: WorldGuard Implementation
Rocket Core Extension
  WG CSR and wgMarker logic
Bus extension – TileLink
  New field for WID
Extension for memory hierarchy
  TLB, I-Cache, D-Cache, Last Level Cache
wgMarker and wg checker
  Standalone generator

## Slide 35: WorldGuard Implementation – wg-aware core
Extend Rocket Core and Tile
Add code snippet
  New CSR
  Control logic
  Propagate WID to downstream (tlb, icache, cache)

## Slide 36: WorldGuard Implementation – bus extension
Rocket SoC employs TileLink Bus
  Use reserved field for user extension
  Simple to extend (no need to modifies all the source files for IO)
  Show code snippet
CustomField
DCache

## Slide 37: WorldGuard Implementation – cache extensions
WID is used for tag matching
  hit if both tag and wid match

## Slide 38: WorldGuard Implementation – Integration to Rocket SoC

## Slide 39: WorldGuard Implementation – Integration to Rocket SoC
Top Module
Simple to connect components

## Slide 40: Related works and future work

## Slide 41: PMP and WorldGuard
“The WorldGuard solution does not replace the RISC-V core Physical Memory Protection (PMP) mechanism or the Memory Management Unit (MMU), but can coexist with those mechanisms.” — SiFive WG Tech. Paper

## Slide 42: PMP and WorldGuard
 | PMP | WorldGuard
Access Check | Performed at core, before any transaction is initiated on the bus Only checked accesses from cores | Performed at the resources, can be out of core Can check accesses from any initiators
Granularity | Limited to #PMP entries (Not scalable) | Limited to #wgChecker entries (Not scalable)
Performance | Need synchronization bet. Cores Need PMP entry update if enclave switch | No need synchronization bet. Cores Need cache sanitization for dynamic config.

## Slide 43: IOMMU and WorldGuard
WorldGaurd
  No address translation
  Region-based permission check
    Coarse-grain due to limited slots
  Small code base
IOMMU
  Address Translation (VA to PA)
    Must access page tables in memory
  Page-based permission check
  Supports virtualized environments
  Itself a device; has own initiator port to access page tables

## Slide 44: WorldGuard > PMP > MMU/IOMMU
WorldGuard provide the coarsest and least-dynamic configurable isolation scheme, and effectively create a few very large worlds in the system at boot time.
Within worlds, PMP can be used to isolate an arbitrary number of physical memory partitions that may vary dynamically.
Within PMP physical memory partitions, MMU and IOMMU provides flexible dynamic page-level translation and protection for both compute and IO

## Slide 45: Collaboration of PMP and WorldGuard for complete isolation
Isolate statically allocated regions (FW, I/O devices) using WorldGuard
  No extra works are required for enclave migration (e.g., PMP updates)
  Useful in Robot, Car, and IoT devices with many sensors
Isolate dynamically allocated regions (OS, enclaves) using PMP
  It is easy for security monitor to reallocate memory region for difference enclaves

## Slide 46: Collaboration of PMP and WorldGuard for complete isolation

## Slide 47: Discussion - Number of World? Number of Slots?
Current Max #Worlds = 32
Current #Slots are not limited to the spec.
  Not increase performance due to parallel address matching and permission check
  But limited to area budget

## Slide 48: Discussion – Core-driven vs. Process-driven

## Slide 49: Discussion – Research topics

## Slide 50: Thank you!
Sungkeun Kim
sk84.kim@samsung.com